# XModem Protocol with CRC
### Introduction
The Xmodem protocol was created years ago as a simple means of having two computers talk to each other. With its half-duplex mode of operation, 128- byte packets, ACK/NACK responses and CRC data checking, the Xmodem protocol has found its way into many applications. In fact most communication packages found on the PC today have a Xmodem protocol available to the user.
### Theory of Operation
Xmodem is a half-duplex communication protocol. The receiver, after receiving a packet, will either acknowledge (ACK) or not acknowledge (NAK) the packet. The CRC extension to the original protocol uses a more robust 16-bit CRC to validate the data block and is used here. Xmodem can be considered to be receiver driven. That is, the receiver sends an initial character “C” to the sender indicating that it’s ready to receive data in CRC mode. The sender then sends a 133-byte packet, the receiver validates it and responds with an ACK or a NAK at which time the sender will either send the next packet or re-send the last packet. This process is continued until an EOT is received at the receiver side and is properly ACKed to the sender. After the initial handshake the receiver controls the flow of data through ACKing and NAKing the sender.
Table 1. XmodemCRC Packet Format
Byte 1	Byte 2	Byte 3	Bytes 4-131	Bytes 132-133
Start of Header	Packet Number	(Packet Number)	Packet Data	16-bit CRC

### Definitions
The following defines are used for protocol flow control.
Symbol	Description	Value
SOH	Start of Header	0x01
EOT	End of Transmission	0x04
ACK	Acknowledge	0x06
NAK	Not Acknowledge	0x15
ETB	End of Transmission Block (Return to Amulet OS mode)	0x17
CAN	Cancel (Force receiver to start sending C's)	0x18
C	ASCII “C”	0x43

Byte 1 of the XmodemCRC packet can only have a value of SOH, EOT, CAN or ETB anything else is an error. Bytes 2 and 3 form a packet number with checksum, add the two bytes together and they should always equal 0xff. Please note that the packet number starts out at 1 and rolls over to 0 if there are more than 255 packets to be received. Bytes 4 - 131 form the data packet and can be anything. Bytes 132 and 133 form the 16-bit CRC. The high byte of the CRC is located in byte 132. The CRC is calculated only on the data packet bytes (4 - 131) .
### Synchronization
The receiver starts by sending an ASCII “C” (0x43) character to the sender indicating it wishes to use the CRC method of block validating. After sending the initial “C” the receiver waits for either a 3 second time out or until a buffer full flag is set. If the receiver is timed out then another “C” is sent to the sender and the 3 second time out starts again. This process continues until the receiver receives a complete 133-byte packet.
### Receiver Considerations
This protocol NAKs the following conditions: 1. Framing error on any byte 2. Overrun error on any byte 3. Duplicate packet 4. CRC error 5. Receiver timed out (didn't receive packet within 1 second) On any NAK, the sender will re-transmit the last packet. Items 1 and 2 should be considered serious hardware failures. Verify that sender and receiver are using the samebaud rate, start bits and stop bits. Item 3 is usually the sender getting an ACK garbled and re-transmitting the packet. Item 4 is found in noisy environments. And the last issue should be self-correcting after the receiver NAKs the sender.

### Sample crc calculation code
int calcrc(char *ptr, int count)
{
    int crc;
    char i;
    crc = 0;
    while (--count >= 0)
    {
        crc = crc ^ (int) *ptr++ << 8;
        i = 8;
        do
        {
        if (crc & 0x8000)
        crc = crc << 1 ^ 0x1021;
        else
        crc = crc << 1;
        } while(--i);
    }
    return (crc);
}
# The Xmodem Protocol Specification

MODEM PROTOCOL OVERVIEW
1/1/82 by Ward Christensen. I will maintain a master copy of
this. Please pass on changes or suggestions via CBBS/Chicago
at (312) 545-8086, or by voice at (312) 849-6279.

NOTE this does not include things which I am not familiar with,
such as the CRC option implemented by John Mahr.

Last Rev: (none)

At the request of Rick Mallinak on behalf of the guys at
Standard Oil with IBM P.C.s, as well as several previous
requests, I finally decided to put my modem protocol into
writing. It had been previously formally published only in the
AMRAD newsletter.

Table of Contents
1. DEFINITIONS
2. TRANSMISSION MEDIUM LEVEL PROTOCOL
3. MESSAGE BLOCK LEVEL PROTOCOL
4. FILE LEVEL PROTOCOL
5. DATA FLOW EXAMPLE INCLUDING ERROR RECOVERY
6. PROGRAMMING TIPS.

-------- 1. DEFINITIONS.
<soh> 01H
<eot> 04H
<ack> 05H
<nak> 15H
<can> 18H

-------- 2. TRANSMISSION MEDIUM LEVEL PROTOCOL
Asynchronous, 8 data bits, no parity, one stop bit.

The protocol imposes no restrictions on the contents of the
data being transmitted. No control characters are looked for
in the 128-byte data messages. Absolutely any kind of data may
be sent - binary, ASCII, etc. The protocol has not formally
been adopted to a 7-bit environment for the transmission of
ASCII-only (or unpacked-hex) data , although it could be simply
by having both ends agree to AND the protocol-dependent data
with 7F hex before validating it. I specifically am referring
to the checksum, and the block numbers and their ones-
complement.
Those wishing to maintain compatibility of the CP/M file
structure, i.e. to allow modemming ASCII files to or from CP/M
systems should follow this data format:
* ASCII tabs used (09H); tabs set every 8.
* Lines terminated by CR/LF (0DH 0AH)
* End-of-file indicated by ^Z, 1AH. (one or more)
* Data is variable length, i.e. should be considered a
continuous stream of data bytes, broken into 128-byte
chunks purely for the purpose of transmission.
* A CP/M "peculiarity": If the data ends exactly on a
128-byte boundary, i.e. CR in 127, and LF in 128, a
subsequent sector containing the ^Z EOF character(s)
is optional, but is preferred. Some utilities or
user programs still do not handle EOF without ^Zs.
* The last block sent is no different from others, i.e.
there is no "short block".

-------- 3. MESSAGE BLOCK LEVEL PROTOCOL
Each block of the transfer looks like:
<SOH><blk #><255-blk #><--128 data bytes--><cksum>
in which:
<SOH> = 01 hex
<blk #> = binary number, starts at 01 increments by 1, and
wraps 0FFH to 00H (not to 01)
<255-blk #> = blk # after going thru 8080 "CMA" instr, i.e.
each bit complemented in the 8-bit block number.
Formally, this is the "ones complement".
<cksum> = the sum of the data bytes only. Toss any carry.

-------- 4. FILE LEVEL PROTOCOL

---- 4A. COMMON TO BOTH SENDER AND RECEIVER:

All errors are retried 10 times. For versions running with
an operator (i.e. NOT with XMODEM), a message is typed after 10
errors asking the operator whether to "retry or quit".
Some versions of the protocol use <can>, ASCII ^X, to
cancel transmission. This was never adopted as a standard, as
having a single "abort" character makes the transmission
susceptible to false termination due to an <ack> <nak> or <soh>
being corrupted into a <can> and canceling transmission.
The protocol may be considered "receiver driven", that is,
the sender need not automatically re-transmit, although it does
in the current implementations.

---- 4B. RECEIVE PROGRAM CONSIDERATIONS:
The receiver has a 10-second timeout. It sends a <nak>
every time it times out. The receiver's first timeout, which
sends a <nak>, signals the transmitter to start. Optionally,
the receiver could send a <nak> immediately, in case the sender
was ready. This would save the initial 10 second timeout.
However, the receiver MUST continue to timeout every 10 seconds
in case the sender wasn't ready.
Once into a receiving a block, the receiver goes into a
one-second timeout for each character and the checksum. If the
receiver wishes to <nak> a block for any reason (invalid
header, timeout receiving data), it must wait for the line to
clear. See "programming tips" for ideas
Synchronizing: If a valid block number is received, it
will be: 1) the expected one, in which case everything is fine;
or 2) a repeat of the previously received block. This should
be considered OK, and only indicates that the receivers <ack>
got glitched, and the sender re-transmitted; 3) any other block
number indicates a fatal loss of synchronization, such as the
rare case of the sender getting a line-glitch that looked like
an <ack>. Abort the transmission, sending a <can>

---- 4C. SENDING PROGRAM CONSIDERATIONS.

While waiting for transmission to begin, the sender has
only a single very long timeout, say one minute. In the
current protocol, the sender has a 10 second timeout before
retrying. I suggest NOT doing this, and letting the protocol
be completely receiver-driven. This will be compatible with
existing programs.
When the sender has no more data, it sends an <eot>, and
awaits an <ack>, resending the <eot> if it doesn't get one.
Again, the protocol could be receiver-driven, with the sender
only having the high-level 1-minute timeout to abort.

-------- 5. DATA FLOW EXAMPLE INCLUDING ERROR RECOVERY

Here is a sample of the data flow, sending a 3-block message.
It includes the two most common line hits - a garbaged block,
and an <ack> reply getting garbaged. <xx> represents the
checksum byte.

SENDER RECEIVER
times out after 10 seconds,
        <--- <nak>
<soh> 01 FE -data- <xx> --->
        <--- <ack>
<soh> 02 FD -data- xx ---> (data gets line hit)
        <--- <nak>
<soh> 02 FD -data- xx --->
        <--- <ack>
<soh> 03 FC -data- xx --->
    (ack gets garbaged) <--- <ack>
<soh> 03 FC -data- xx ---> <ack>
<eot> --->
        <--- <ack>

-------- 6. PROGRAMMING TIPS.

* The character-receive subroutine should be called with a
parameter specifying the number of seconds to wait. The
receiver should first call it with a time of 10, then <nak> and
try again, 10 times.
After receiving the <soh>, the receiver should call the
character receive subroutine with a 1-second timeout, for the
remainder of the message and the <cksum>. Since they are sent
as a continuous stream, timing out of this implies a serious
like glitch that caused, say, 127 characters to be seen instead
of 128.

* When the receiver wishes to <nak>, it should call a "PURGE"
subroutine, to wait for the line to clear. Recall the sender
tosses any characters in its UART buffer immediately upon
completing sending a block, to ensure no glitches were mis-
interpreted.
The most common technique is for "PURGE" to call the
character receive subroutine, specifying a 1-second timeout,
and looping back to PURGE until a timeout occurs. The <nak> is
then sent, ensuring the other end will see it.

* You may wish to add code recommended by Jonh Mahr to your
character receive routine - to set an error flag if the UART
shows framing error, or overrun. This will help catch a few
more glitches - the most common of which is a hit in the high
bits of the byte in two consecutive bytes. The <cksum> comes
out OK since counting in 1-byte produces the same result of
adding 80H + 80H as with adding 00H + 00H.